# Downgrading the Xbox360

## Introduction

Downgrading is a two stage process, first a “downgrader” flash image is created by combining data from a dump of your current, working, XBox flash and a set of original 2.0.1888 files. The Kernel is to be downgraded to 2.0.1888 and it is necessary to recreate the 2.0.1888 Filesystem.

The new image contains CB pairing data modified such that the “lockdown counter” is correct and will allow the 2.0.1888 Kernel to boot without any patches from CF/CG sections being applied. Since the CPU keys are not known at this stage it is not possible to calculate the correct hash for the region of CB that contains the new pairing data. Without this hash the Xbox will refuse to boot and fails with a POST code of 0xA4. The new, “downgrader”, flash image is written to the XBox flash and an exhaustive search algorithm applied to find the correct hash and thus allow the original 2.0.1888 Kernel to be booted.

Once the correct hash has been found and the 2.0.1888 Kernel can be booted you may update your console to a vulnerable version (4532 or 4548) and obtain the CPU keys for your Xbox. The process is not described in this document.

## Before You Begin…

You will need the following:

- Xbox360 with Infectus chip and a PIC interface installed

- The Degraded Application (Degraded.exe) in a directory on your HDD

- The Downgrade Tool (DGTool.exe, Infectus.dll and SiUSBXp.dll) in a directory on your HDD

- The contents of the original 2.0.1888 filesystem, unpack the file 1888.FS.rar to a directory on your hard drive.

- A dump of your Xbox Flash obtained using the Infectus chip.

## The PIC Interface

### Installation

The PIC Interface is connected to the Host PC by a 9 pin serial connection. For the connection to the XBox I suggest using a 16 way IDC header. Power is supplied by a USB connection on the Host PC (cut an old USB cable down and use the +5 and 0V wires).

| IDC Pin | Name | Xbox Motherboard connection |
| --- | --- | --- |
| 1 | POST[0] | FT6U1 |
| 2 | POST[1] | FT6U7 |
| 3 | POST[2] | FT6U6 |
| 4 | POST[3] | FT6U5 |
| 5 | POST[4] | FT6U4 |
| 6 | POST[5] | FT6U3 |
| 7 | POST[6] | FT6U2 |
| 8 | POST[7] | FT6U8 |
| 9,10 | 0V |  |
| 15 | JTAG Reset | J8C1 Pin 2 |
| 16 | NAND Flash CE | Infectus Pin N |

Table 1 Suggested 16 Way IDC Header Pinout

Figure 1 The POST Port

### The PIC Serial Interface

It is possible to communicate with the PIC via Hyperterminal (or any other terminal software). The Serial port should be set to 19200 baud, 8 data bits, No parity,1 stop bit.

The PIC will respond to the following commands

| Command | Response | Comment |
| --- | --- | --- |
| ‘?’ | ‘!X’ | Gets status of JTAG Reset line, X=0 (Reset line floating, CPU running) X=1 (Reset line held low, CPU reset) |
| ‘r’ | ‘Reset’ | Forces JTAG Reset low |
| ‘g’ | ‘Running…’ | Allows JTAG Reset to float |
| ‘p’ | POST Mon | Enters POST monitor mode |
| ‘m’ | ‘XXXX’ or ‘E YY’ | Performs a timing measurement, the PIC will respond with either: A timing measurement (Where XXXX is the timing measurement in hex) An error code (Where YY is the value read from the POST bus) |

Figure 2 PIC Interface Commands

## Creating the “Downgradable” Image

To create the “downgrader” image start the Degraded tool:

Figure 3 The Degraded Application

First, click the “Settings” button and verify the following:

1) 1BL Key is “DD88AD0C9ED669E7B56794FB68563EFA”

2) 1888 File System is the directory where you unpacked the 1888.FS.rar file.

3) File System Start should be set to 39

Figure 4 The Settings Dialog

Next, load your flash dump by clicking the “…” button and selecting the file, the Degraded tool will display information extracted from the dump.

To create the “downgrader” image click on the “Build Downgrader Image” button and select a directory and filename to save the “downgrader”. Exit the Degraded tool.

## Verifying your Setup

1) Attach the PIC interface to the Xbox and the host PCs serial port, the Xbox should be connected to the power supply (orange light) but turned off.

2) Write the “downgrader” image to the Xbox flash using the Infectus chip.

3) Apply power to the PIC interface but leave the Xbox powered off.

4) Start you terminal application and verify communications with the PIC by sending a ‘?’.

5) The PIC will reply with ‘!0’ or ‘!1’ depending on the state of the JTAG Reset line.

6) Send a ‘p’ to enter POST Port monitor mode (the PIC will respond with POST Mon (Reset PIC to exit) ).

7) Power on the XBox and observe its POST sequence, you should see 5 attempts to boot each ending in code A4 before the RRoD

P 00

P 10

P 11

P 12

P 18

P 19

P 1A

P 1B

P 1C

P 1D

P 1E

P 20

P 21

P A4

8) Power off the XBox and reset the PIC.

9) Send the ‘r’ command to hold the XBox CPU in reset

10) The PIC should respond ‘Reset’

11) Verify it by sending the ‘?’ command.

12) The PIC should respond ‘!1’

13) Power on the XBox and wait for the RRoD

14) Send the ‘m’ command

15) After approximately 1 second  the PIC should respond with a timing measurement or an error code.

45b4

45bf

45b7

45b6

Repeat steps 14 & 15 several times. If you are seeing repeated and similar 4 digit Hex values (and the hashing LED blinks) then the system is working correctly and ready to downgrade.

NOTE: Occasionally you may see the following error codes:

E 96

This error code indicates that the CB block has become corrupt and the XBox flash should be erased and the original “downgrader” image reloaded.

E 15

Sometimes the Infectus and South Bridge can cause a conflict on the flash bus, this error code indicates that this has happened. Power off the Xbox, remove the USB cable from the Infectus, remove and then replace the Xbox power cable, replace the Infectus USB cable and try again.

## Searching for the CB Hash

To run the downgrade tool you should copy the “downgrader” image generated previously to the directory on your HDD where the Downgrade Tool was copied.

- Verify the PIC interface is powered up.

- Start a command prompt and ‘cd’ to the directory where the Downgrade Tool is located.

- Run the Downgrade Tool at the command prompt

- Power on the Xbox and wait for the RRoD

- Press a key to begin the process.

- Wait 2-3 hours

The Downgrade Tool requires a minimum of 2 command line parameters:

DGTool N File

Where N is the number of the Comm Port you have connected to the PIC interface and File is the “downgrader” image generated previously. The Downgrade Tool will examine the “downgrader” image and begin the process of searching for the correct CB hash. The Downgrade Tool outputs information as it runs:

Using Comm Port 6

"Downgrader" File 1888G.raw

Pairing Data 0x38695E 02

H[16 00000000000000000000000000000000]

Initial Hash:

H[0 XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX]

Turn on your Xbox, press any key when the RRoD starts

H[0 00XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17846 A 17844 D 3 : 0 NEXT

H[0 01XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17843 A 17843 D 0 : 0 NEXT

H[0 02XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17846 A 17844 D 3 : 0 NEXT

H[0 03XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17847 A 17844 D 3 : 0 NEXT

H[0 04XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17839 A 17843 D 0 : 0 NEXT

H[0 05XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17842 A 17843 D 0 : 0 NEXT

H[0 06XXXXXXXXXXXXXXXXXXXXXXXXXXXXXX] M 17847 A 17843 D 4 : 0 NEXT

The information displayed is:

- The index into the hash currently being tested and the hash written to the flash.

- The timing measurement for this hash.

- The average timing measurement for this hash index

- The difference between the measurement and the average.

- A “confidence” figure

- The search algorithms decision on the candidate byte.

The timing measurement is compared to the average and the difference calculated, based on this and the confidence figure a decision is made

diff = measurement – average;

if ( diff > threshold_2 )

confidence += 2;

if ( confidence >= 12 )

return HIT;

else

return REPEAT;

if ( diff > threshold_1 )

if ( confidence > 0 )

confidence -= 1;

return REPEAT;

if ( confidence > 0 )

confidence -= 1;

return REPEAT;

return NEXT;

A candidate byte must acheive a “confidence” figure of 12 or above to be declared correct. The “confidence” figure mitigates the effect of jitter in the timing measurements, reducing the chance of mis-guesses while maximizing the chance of detecting a correct candidate byte. It also results in an average of >1 measurements being made per candidate byte. A candidate byte is tested a minimum of 6 times before it is declared valid:

H[13 4F700DF50BB8B8EFFC928B1CCE20XXXX] M 17992 A 17987 D 5 : 0 NEXT

H[13 4F700DF50BB8B8EFFC928B1CCE21XXXX] M 17990 A 17987 D 3 : 0 NEXT

H[13 4F700DF50BB8B8EFFC928B1CCE22XXXX] M 17986 A 17987 D 0 : 0 NEXT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 17999 A 17987 D 12 : 2 RPT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 18005 A 17987 D 18 : 4 RPT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 18007 A 17987 D 20 : 6 RPT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 17999 A 17987 D 12 : 8 RPT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 17999 A 17987 D 12 : 10 RPT

H[13 4F700DF50BB8B8EFFC928B1CCE23XXXX] M 18004 A 17987 D 17 : 0 HIT!

Eventually all 16 bytes will be found and the Xbox will attempt to continue the boot process. Turn off the Xbox and disconnect the PIC interface.

H[15 4F700DF50BB8B8EFFC928B1CCE23EB1F] M 18008 A 18009 D 0 : 0 NEXT

H[15 4F700DF50BB8B8EFFC928B1CCE23EB20] M 18013 A 18010 D 4 : 0 NEXT

H[15 4F700DF50BB8B8EFFC928B1CCE23EB21] M 18008 A 18009 D 0 : 0 NEXT

H[15 4F700DF50BB8B8EFFC928B1CCE23EB22] M 18009 A 18009 D 0 : 0 NEXT

H[15 4F700DF50BB8B8EFFC928B1CCE23EB23] M 18009 A 18009 D 0 : 0 BOOT!

Unfortunately, things go wrong sometimes.

Very occasionally a correct candidate byte is missed, the algorithm will cycle through all 256 possible candidate bytes until it finds the correct one or it is stopped.

If the process is interrupted before it is completed you can restart at that point with 2 extra command line parameters:

DGTool N File X YY…YY

Where X is the number of known hash bytes and YY…YY are the bytes themselves. If the last guess before the process was interrupted is:

H[8 4F700DF50BB8B8EF22XXXXXXXXXXXXXX] M 17933 A 17932 D 1 : 0 NEXT

Then 8 bytes (4F700DF50BB8B8EF) have been found and the command line parameters:

DGTool 6 1888G.raw 8 4F700DF50BB8B8EF

Will restart the process at the point where it was interrupted.

Using Comm Port 6

"Downgrader" File 1888G.raw

Pairing Data 0x38695E 02

H[16 00000000000000000000000000000000]

Initial Hash:

H[8 4F700DF50BB8B8EFXXXXXXXXXXXXXXXX]

Turn on your Xbox, press any key when the RRoD starts

Even more occasionally an incorrect candidate byte will be selected, this will be quite obvious for 2 reasons

- The algorithm will loop for ever, never finding another correct candidate.

- There will be a large number of large negative measurements and the average will fall by 10 to 11 units.

Interrupt the process and restart it, use the command line options to restart the process but reduce the number of known hash bytes by 1 to retry the incorrect guess.

## Finally

Your Xbox should now boot and prompt you to select your language etc etc. You should obtain and apply an update that contains a vulnerable kernel (4532 or 4548) and obtain your CPU fuse data. The CB section will still contain a “suspicious” version lockdown number and once the CPU fuse data is available this should be fixed using the NAND flash dump tool. Either patch the CB version lock down to 0 in your new, vulnerable image or increment the CF lock down version by 1 in your original flash image (the 4532 update will blow another eFuse). Reflash your Xbox.

## Known Problems

Sometimes the Downgrader Tool will hang when it starts, this appears to be due to the Infectus being in a strange state. Power off the Xbox, remove the USB cable from the Infectus, remove and then replace the Xbox power cable, replace the Infectus USB cable and try again.